## Slide 1
TECHNICAL DOCUMENTATION
Multimodal Deep Learning
Sensors, Camera & Fusion Architecture
AI-Powered Portable Breast Lump Detection Device
Modalities
2 (Thermal + Pressure)
Sensors
8× FSR + 1 Thermal Camera
Cost
~$110 Hardware
Veekshitha | 2026

## Slide 2
Document Overview
1
Multimodal Learning
What it is, why two modalities, model overview
2
Fusion Architecture
Feature fusion, concatenation, step-by-step process
3
Thermal Camera
MLX90640 — how it works, pin connections, image processing
4
FSR Pressure Sensors
DF9-16 sensors, voltage divider, wiring all 8
5
Arduino UNO
Role in system, reading sensors, serial to Python
6
Software Requirements
All libraries, versions, installation commands

## Slide 3
1. Multimodal Deep Learning
What is Multimodal Learning?
Multimodal deep learning trains a model on two or more different types of data simultaneously, combining them into one prediction. In this project: thermal infrared images + numerical pressure sensor readings.
Thermal Only
✅ Detects heat from tumour blood supply
⚠️ Affected by room temperature. Surface level only.
Pressure Only
✅ Detects tissue stiffness. Mimics doctor palpation.
⚠️ Cannot detect deep or soft tumours.
Multimodal ✅
✅ Thermal catches what pressure misses and vice versa.
⚠️ Best accuracy. Fewer false results.
This project mirrors how a doctor works — simultaneously SEES thermal patterns and FEELS tissue stiffness before diagnosing.

## Slide 4
2. Fusion Architecture — Step by Step
Thermal Branch
Input 224×224×3
VGG16 (frozen)
Flatten 25088
Dense(512) ReLU
Dense(256) ReLU
→ 128 features
Pressure Branch
Input 30 features
Encoder 128→64
Encoder 32→16
Bottleneck (16)
Dense(32) ReLU
→ 16 features
Fusion Model
Concat(128+16=144)
Dense(256) + BatchNorm
Dropout(0.4)
Dense(128) + BatchNorm
Dropout(0.3)
Dense(1) + Sigmoid
Output: Healthy / Abnormal + Confidence %
128 thermal features + 16 pressure features = 144 concatenated features → Fusion Input

## Slide 5
3. Thermal Camera — MLX90640
MLX90640 Specifications
Resolution:
32×24 pixels = 768 readings
Voltage:
3.3V ONLY (not 5V!)
Interface:
I2C (SDA + SCL)
I2C Address:
0x33
I2C Speed:
400kHz Fast Mode
Temperature:
−40°C to +300°C, ±1.5°C
Field of view:
55° × 35°
Refresh rate:
0.5 Hz to 64 Hz
How It Detects Cancer
Tumours have increased blood flow → area is 0.5–2°C warmer than surrounding tissue → thermal camera detects this hotspot → CNN classifies the thermal pattern as abnormal.
Pin Connections to Arduino UNO
VCC
→ 3.3V
Power — 3.3V ONLY, NOT 5V!
GND
→ GND
Ground reference
SDA
→ A4
I2C Data — sends data to Arduino
SCL
→ A5
I2C Clock — sync speed
⚠️ CRITICAL: Camera uses 3.3V. Connecting to 5V will permanently damage the MLX90640 sensor.

## Slide 6
4. FSR DF9-16 Pressure Sensors
What is an FSR Sensor?
FSR = Force Sensitive Resistor. Changes electrical resistance when pressure is applied. No pressure → high resistance (~1MΩ). Hard press → low resistance (~200Ω). Arduino reads this as 0–1023.
Voltage Divider Circuit
5V → FSR → junction → 10kΩ → GND
Arduino reads voltage at junction (A0–A7)
Formula: V = 5V × 10kΩ / (FSR + 10kΩ)
Not pressed: ~10 | Light press: ~512 | Hard: ~1003
Sensor
FSR Leg 1
Arduino Pin
Resistor to GND
FSR 1
5V
A0
10kΩ
FSR 2
5V
A1
10kΩ
FSR 3
5V
A2
10kΩ
FSR 4
5V
A3
10kΩ
FSR 5
5V
A4
10kΩ
FSR 6
5V
A5
10kΩ
FSR 7
5V
A6
10kΩ
FSR 8
5V
A7
10kΩ
KEY: FSR leg 2 + resistor top leg + signal wire all go into the SAME breadboard column — this is the junction point.

## Slide 7
Thermal Image Processing Pipeline
1
Read Camera
768 float values from MLX90640 via I2C (32×24 grid)
2
Reshape
Reshape to 24×32 NumPy array
3
Normalise
(value−min)/(max−min)×255 → 0 to 255 range
4
Colormap
Apply inferno colormap: black=cold → yellow=hot
5
Upscale
Bicubic interpolation: 32×24 → 224×224 pixels
6
Preprocess
VGG16 preprocess_input (subtract ImageNet mean)
7
Inference
Reshape to (1,224,224,3) → CNN prediction
Why inferno colormap? It matches the training dataset (DMR-IR) which uses the same colormap — reducing domain gap.

## Slide 8
5. Arduino UNO — Reading Sensors
Arduino UNO Specs
Microcontroller:
ATmega328P
Analog pins:
A0–A7 (8 pins)
ADC resolution:
10-bit (0–1023)
I2C pins:
A4 (SDA) + A5 (SCL)
Baud rate:
9600 bps
Programming:
C++ in Arduino IDE
Power:
5V via USB from laptop
Role:
Read 8 FSR + send via Serial
Arduino Sketch (fsr_reader.ino)
void loop() {
int s1 = analogRead(A0); // 0-1023
int s2 = analogRead(A1);
// ... repeat A2 to A7
Serial.println("234,187,312,298");
delay(100);
}
Python Serial Reader (read_arduino.py)
import serial
ser = serial.Serial(
'/dev/cu.usbserial-1410', 9600)
line = ser.readline().decode('utf-8')
values = [int(x) for x in line.split(',')]
# [234, 187, 312, 298, 201, 267, 189, 344]
Data flow: FSR sensors → Arduino reads → USB Serial → Python pyserial → Flask API → AI inference → Web app result

## Slide 9
6. Complete Software Requirements
Python Libraries
tensorflow-macos
2.13.0
Deep learning (Mac M1)
tensorflow
2.13.0
Deep learning (Windows/Linux)
tensorflow-metal
1.1.0
Apple Metal GPU (Mac)
numpy
latest
Array operations
pandas
latest
Data loading and CSV
scikit-learn
latest
Preprocessing + metrics
pillow
latest
Image loading/resizing
flask + flask-cors
3.0+
REST API backend
reportlab
latest
PDF report generation
pyserial
latest
Arduino USB serial
Frontend Requirements
Node.js 18+
JavaScript runtime
React 18
Frontend UI
Vite 5
Dev server + build
react-router-dom
Page routing
axios
HTTP API calls
Installation Commands
conda create -n breastkit python=3.11
conda activate breastkit
pip install tensorflow-macos==2.13.0
pip install flask flask-cors pillow
pip install numpy pandas scikit-learn
pip install pyserial reportlab joblib
cd frontend && npm install

## Slide 10
Complete System Summary
Multimodal
2 modalities: Thermal image CNN (128-dim) + Pressure autoencoder (16-dim) → fused 144-dim
Fusion
Feature concatenation + Dense(256)→Dense(128)→Dense(1) sigmoid output
Thermal CNN
VGG16 transfer learning, 96.39% accuracy, 96.71% AUC, threshold 0.10
Pressure
Autoencoder anomaly detection (healthy-only), 96.51% accuracy, 100% AUC
Camera
MLX90640: 32×24 IR, 3.3V, I2C on A4/A5, 32×24→224×224 with inferno colormap
Sensors
8× FSR DF9-16 + 10kΩ voltage dividers → Arduino A0–A7 → USB serial 9600
Software
Python 3.11 + TF 2.13 + Flask 3.0 + React 18 + Node.js 18 + Arduino IDE 2
Cost
~$110 total hardware. Clinical equivalents cost $50,000+.
Thank you | Questions? | GitHub: github.com/veeksh07/AI-Powered-Portable-Breast-Lump-Detection-Device